## Slide 1: The quantitative Working Space Model - Evalucao
Florian Schmitt, M.Sc.
Institute for product development and machine elements pmd
Technical University of Darmstadt

## Slide 2: Agenda
Metodologia qWRM
4
Exemplos de qWSM
3
O modelo qWSM
2
Objetivos
1

## Slide 3: Objetivos e caminho da pesquisa
Objetivos:
Melhoria da compreensão do sistema
Comparação entre o uso do qWSM e sem usar o qWSM
Cada grupo deve derivar três analises funcionais do próprio sistema para explicar a função:
Análise conceitual
Análise dos parâmetros de design
Análise ambiental

## Slide 4: Agenda
Metodologia qWRM
4
Exemplos de qWSM
3
O modelo qWSM
2
Objetivos
1

## Slide 5: State of Research – Competing Modelling Approaches
Source: Matthiessen 2019;
“During an engineering design process, designers create sequences of product models by switching between product models with different purposes. To enable an efficient use of these product models, researchers are required to anticipate the compatibility of the models in application by designers.” Matthiessen et al. 2024
Ecolha uma opção cada pergunta e objetivo de modelagem. Ou não?

## Slide 6: State of Research – The Working Space Model (WSM)
O quantitative Working Space Model (WSM) Serve como uma representação baseada em volume de sistemas. O modelo permite que os profissionais derivem uma relação entre a incorporação de um sistema técnico e suas:
Funções
Disfunções
Não-funções
Os insights derivados do modelo podem ser usados para superar as deficiências de sistemas existentes, como vazamentos."
Working Surface
Working Surface Pair
Working Space
WS 1
WS 2
WS 3
Notes: As most approaches of system representations, the qWSM derives a simplification of a technical system and serves as a way to explain the functions of a system.
What is special about the qWSM is the volume based approach, making it suitable to describe the system behavior based on balancing conservation quatitites such as charge, or energy.
Doing so, patrictioners can derive a relation between the embodiment of technical system and it‘s functions., mal- and so called non functions.
The qWSM was developed to systematically identify and describe the determining design parameters and to find existing shortcomings.
The main model elemets are the working space, a 3 dimensional space, filled with mater in solid, fluid or gasoeus state, it‘s suface and the coupling of working spaces to each other, the so called working surface pair. Only if a WSP is present where a function such as sealing should be conducted, the system can drive it‘s inteded functions. On the right sight we can see the cross sectional view of a radial shaft seal and the major working spaces.
Usign Fig low
WSM separates Systems into Subvolumens (Working Spaces) their surfaces, and boundary areas, WSP.
On WSP all kinds of functions are conducted, WSs are affected by introduces quantities such as particles, Energy, Force.
Functions, Mal/
Nonfunctions  No WSP where needed
Insights of the model enable practitioners to redesign systems in order to overcome shortcomings. (Leakage)

## Slide 7: State of Research – The quantitative Working Space Model (qWSM)
Eq: (Bauer, 2021)
WS 1,
    Descrevendo o comportamento de sistemas técnicos, por meio de:
      Explicação da função,
      Possíveis disfunções e não-funções,
      Geração de uma representação quantitativa
    antes de detalhar o design.
    Identificação de quantidades que determinam a função dos sistemas:
      Componentes críticos
      Parâmetros de design
      Correlação entre parâmetros de design e comportamento do sistema
    Modelagem multifísica em diferentes domínios
Notes: So let’s go a little bit more into detail.
The models aim is to describe the behavior of a technical system. We want to understand how main and auxiliary functions work, which working spaces contribute to them, predict possible mal- and non functions and to generate a quantitative representation of the system.
The degree of detail is limited to the maturity of the development process and can increases throughout the process.
Why can? Because in the first place the objective is to understand the system before elaborating the embodiment.
We wand to identify which critical working spaces or components contribute to the functions we want to analyze, which design parameters affect them and to derive a correlation between those and the systems behavior. Doing so we can achieve a multiphysical model across different physical domains such as hydrodynamic and electric domain as the qWSM working principle is the balance of conservation quantitates. For the example of the radial shaft seal we can identify the sealing surface of the seal as the area of interest, the seal as the critical component and it’s shape in terms of a surface relations as the function determining design parameter. Doing so we can achieve a quantitative relation between design parameters and function for a simplified systems representation.

## Slide 8: Elementos de qWSM
WS = Working Space:
espaço tridimensional
Pode conter sólidos, líquidos, meios gasosos ou vácuo
Um aingulo WS geométrico pode ser representado em vários WS de ação de diferentes dimensões.
Working surface
Superfície de um WS, limita geometrico do espaço
WSP Working surface pair
Forma-se apenas entre WS que interagem funcionalmente.
Essa interação pode ser caracterizada pelo transporte de energia, matéria, sinal ou informação.
Cada interação pode ser descrita por uma troca de grandezas conservativas (energia, carga, massa, impulso).
Notação tem uma direção: WSP_1-2 significa fluxo de WS2 a WS1

## Slide 9: Elementos de qWSM
Ambiente
Ambiente do sistema.
Pode ser descrito como um espaço holístico,
  preenchido com meios, ou
  aberto.
Interações relevantes com o sistema são descritas como WSP (Pares de Superfícies de Trabalho) com os WS (Espaços de Trabalho) externos.
A fronteira do sistema pode variar.
Estruturas residuas
Estruturas contidas no sistema que não são funcionalmente relevantes.
São consideradas apenas geometricamente, não modeladas funcionalmente.
Por exemplo:
superfícies de delimitação não relevantes
Geometrias internas em líquidos em repouso

## Slide 10: Motivaçãlo and objetivo
    Estrutura para a criação de Working Space Models:
    Descrever o comportamento de sistemas técnicos, por meio de:
    Explicação da função, possíveis disfunções ruins e não-funcionais
    Geração de uma representação quantitativa antes de detalhar a incorporação.
    Identificação das quantidades que determinam o comportamento do sistema
    Componentes críticos
    Parâmetro de design
    Correlação entre os parâmetros de design e o comportamento do sistema
    Modelagem multifísica em diferentes domínios fisicos
Notes:     Tool to describe the behavior of technical systems,
      Explaining the function, possible mal- and non functions
      generating a quantitative representation
    Giving insights on possibly occurring mal- and non functions before detailing the embodiment
    Identifying quantities that determine the systems behavior
          Correllation between desing parameters and system behavior
          Corellation between physical domains
    Prepartion for simulation
    Identifying crictical componets/ design parameter
    Describing the nature of the simulative problem (e.g. time variant /invariant)

## Slide 11: Agenda
Metodologia qWRM
4
Exemplos de qWSM
3
O modelo qWSM
2
Objetivos
1

## Slide 12: Exemplo 1 Tanque termico
WS_1
WS_5
WS_2
WS_3
WS_4
WS_6
WSP_6-ambiente
WSP_5-4
WSP_3-ambiente
WSP_4-3
WSP_4-1
WSP_1-2
WSP_2-ambiente

## Slide 13: Ram Pump

## Slide 14: The Hydraulic Ram – an example for using the qWSM
Reference: Von Jorge Czajkowski - propia, CC BY-SA 2.5, https://commons.wikimedia.org/w/index.php?curid=2062378
Características:
Conceito de bombeamento, acionado apenas por água
Sem necessidade de sistemas de controle, sem componentes elétricos
Aplicável em comunidades localizadas em áreas remotas
Sistemas robustas
Princípio de funcionamento?
Parâmetros de design relevantes?
Notes: To illustrate the basic idea how to use the qWSM during the development process we will discuss an exemplary development project.
Development objective: Design a reliable source of potable water for a remotely located village.
Hydraulic ram.
What is the hydraulic ram? / Characteristics
Pump driven by the water itself, eg. River.
No electronics, no control systems
Applicable in remote locations.
But how does it work?
What are the function determining design parameters and what are the limitations of the concept?
Potable Water: with low risk of pollution (low population, no industry or livestock close to the natural spring)

## Slide 15: Agenda
Metodologia qWRM
4
Exemplos de qWSM
3
O modelo qWSM
2
Objetivos
1

## Slide 16: The hydraulic ram – conceito
WS 2
Outlet
WS1
Water-Reservoir
WS3
g
Notes: Here we can see a simplified representation of an hydraulic ram.
Focus on most important working spaces for working principle
Only structured, no calculations possible yet
Click
By connecting the working spaces and describing their relations as well as quantifying their characteristics in terms of geometry the derivation of state and coupling equations becomes possible!
Now calculations are possible
How can we find the function determining design parameters?
First assumption: where are working spaces that change their shape/boundaries or their state variable significantly?
WS 2, at WSP leak.
Most important WSPs: WSP_leak & WSP 2_3

## Slide 17: The hydraulic ram – principio e parametros carateristicos
Efeito dominante: Conservação do momento
Parâmetro crítico de design: Área da seção transversal e comprimento do tubo
Notes: Remember:
As no external Energy is introduced except of the water itself, we need to explain the concept by the redirection of the flow of water.
As momentum can not be transformed to eg. Temperature in a instant, but the valve is closing very fast, the momentum of the water in WS 2 is redirected into WS 3, being open.
After some calculations we can derive the following equation:
The achievable discharge head about the level of the water inlet is a function of the introduced kinetic energy of the supplying water and the design parameters.
The discharge head becomes describable as a function of area, length and v_in
Not only identifying the design parameters right from an early development stage but also describing the effects of their changes within one comprehensive representation.
The equation is a simplification and neglecting the effect of friction as well as characteristics of valves, and turbulence. Therefor it is only an orientation
For finding the limitations of the pumping concept, the granularity of the model must be increased to describe the neglected effects!

## Slide 18: Analise ambiental
Reference: Pixabay
qWSM
Clima?
Geografia!
Notes: After introducing the idea of the qWSM model we want to have a look into the application as a tool within K Space.
We keep the aforementioned example and try to structure the development process.
Development objective:
Design a water supply for a remotely located village
No access to reliable energy supply
Supply of potable water due to river with low risk of pollution (low population, no industry or livestock close to the natural spring)
Dry area, rain only during rain season
River significantly lower than the village
Efficiency is less important than energy supply

## Slide 19: Objetivos e caminho da pesquisa
Coleta de dados por meio de questionários online
16.10
30.10
06.11
Participacao obrigatorio, sem influenca da nota da disciplina
Responder as questionarios online
Distribução das tutorials en eDisciplinas

## Slide 20: Questionario 1: Conceito
Queremos entender quais são as partes ou subsistemas mais importantes em relação à função do seu sistema!
Identificar as partes que definem as principais funções do seu sistema.
Derivar uma estrutura funcional do seu sistema.
Derivar uma relação qualitativa entre os parâmetros de design e a função do seu sistema!

## Slide 21: Questionario 2: Design
Queremos entender, a relação quantitativo entre o subsistema mais importante da função do seu sisteme e os parâmetros de design e processo!
Identificar os partes de seu sistema envolvidos na função da zona de design
Nomei os parâmetros de design e os parâmetros de processo que foram identificados responsavel para a função.
Derivar a relação quantitativo entre a função da zona de design e os parâmetros de design e processo definidos

## Slide 22: Questionario 3: Analise ambiental
Queremos entender a interação do sistema com o ambiente.
Desenvolver uma visualização das zonas de interação com o ambiente.
Descrever as relações de interação qualitativa e quantitativa.
Derivar a relação de todas as interações do seu sistema com o ambiente. → Quais são os subsistemas e parâmetros de design afetados?

## Slide 23: Methodological framework for building a qWSM
How to organize multiple qWSMs for the same geometric model?
Topological organization
Graph theory
Sheaf Theory

## Slide 24: Thank you for your attention!
I am looking forward to your questions!
Please feel free to contact me for any further questions:
florian.schmitt@tu-darmstadt.de
+49 6151 16-21170

## Slide 25: References
[1] Grauberger, P., Wessels, H., Gladysz, B., Bursac, N., Matthiesen, S., & Albers, A. (2020). The contact and channel approach – 20 years of application experience in product engineering. Journal of Engineering Design, 31(5), 241–265. https://doi.org/10.1080/09544828.2019.1699035
[2] Franke, H.‑J., & Kaletka, I. (1996). Hilfsmittel zum Auffinden einer ersten Gestalt beim methodischen Konstruieren: Gestaltbeeinflussung durch die Verwendung physikalischer Effekte. Forschung Im Ingenieurwesen, 62(10), 265–270.
[3] Albers, A., & Wintergerst, E. (2014). The Contact and Channel Approach (C&C 2-A): Relating a system’s physical structure to its functionality. In An Anthology of Theories and Models of Design (pp. 151–171). Springer.
[4] Matthiesen, S., Grauberger, P., Bremer, F., & Nowoseltschenko, K. (2019). Product models in embodiment design: an investigation of challenges and opportunities. SN Applied Sciences, 1(9). https://doi.org/10.1007/s42452-019-1115-y
[5] Matthiesen, S., Grauberger, P., Hölz, K., Nelius, T., Bremer, F., Wettstein, A., Gessinger, A., Pflegler, B., Nowoseltschenko, K., & Voß, K. (2018). Modellbildung mit dem C&CAnsatz in der Gestaltung - Techniken zur Analyse und Synthese.
[6] Beetz, J.‑P., & Kirchner, E. (2019). Das Wirkraummodell – Ein Hilfsmittel bei der Gestaltung sauberkeitsrelevanter Produkte. Forschung Im Ingenieurwesen, 83(4), 933–946. https://doi.org/10.1007/s10010-019-00375-0
[7] Beetz, J.‑P., Schlemmer, P. D., Kloberdanz, H., & Kirchner, E. (2018). Using the new Working Space Model for the development of hygienic products In Design Conference Proceedings, Proceedings of the DESIGN 2018 (pp. 985–996). The Design Society, Glasgow, UK. https://doi.org/10.21278/idc.2018.0142
[8] Kraus,B., Schmitt F., Steffan k.-E., Kirchner E., A valve closing body as a central sensory-utilizable component, Procedia CIRP, Volume 100, 2021, p. 109-114, ISSN 2212-8271, https://doi.org/10.1016/j.procir.2021.05.018.

## Slide 26
[9] Schösser, F., Schmitt, F*., Kirchner, E., and Breimann, R.: Influence of the operation strategy on the energy consumption of an autonomous sensor node, Journal of Sensors and Sensor Systems., Volume 11, 263–275, https://doi.org/10.5194/jsss-11-263-2022, 2022.
[10] Schmitt, F; Kirchner, E The quantitative Working Space Model – Generating Knowledge in the K Space. In: DS 118: Proceedings of NordDesign 2022 : Copenhagen, Denmark, 16th - 18th August 2022, S. 1-12, ISBN 9781912254170, DOI: 10.35199/norddesign2022.17,
[11] Hatchuel, A., Le Masson, P., & Weil, B. (2017). C-K Theory: Modelling Creative Thinking and Its Impact on Research. In F. Darbellay, Z. Moody, & T. Lubart (Eds.), Creativity in the Twenty First Century. Creativity, Design Thinking and Interdisciplinarity (pp. 169–183). Springer Singapore. https://doi.org/10.1007/978-981-10-7524-7_11
[12] Hatchuel, A., & Weil, B. (2003). A new approach of innovative design: an introduction to CK theory. The International Conference on Engineering Design.
[13] Hatchuel, A., & Weil, B. (2009). C-K design theory: an advanced formulation. Research in Engineering Design, 19(4), 181–192. https://doi.org/10.1007/s00163-008-0043-4
[14] Plenary speech auf dem: “16h International Paris Workshop of the Design Theory SIG of the Design Society” Design Theory Workshop der Special Interest Group der Design Society in Paris am 30.01.2023
[15] Steffan K.-E., Schmitt, F.*, Kraus J.-P., Freudenberg J., Kirchner E. Application of Manufacturing Induced Properties to Exploit the Potentials of a Hybrid Integrating Additive Manufacturing Technology: 33rd CIRP Design Conference, Sydney, Australia,
[16] Schmitt, Florian; Rudolph, Kris; Kirchner, Eckhard; Blat-Belmonte, Benjamin; Kappes, Aaron; Rinderknecht, Stephan: Smart Products, Engineering and Services. An example of modern engineering education. At: SEFI 50th Annual conference of The European Society for Engineering Education. " Barcelona: Universitat Politècnica de Catalunya, 2022, p. 2184-2188. DOI 10.5821/conference-9788412322262.1197.
[[17] Beetz, J.-P. Modelle und Methoden zur systematischen Entwicklung hygienegerechter Produkte, Dissertation TU Prints: Tu Darmstadt, Darmstadt 2018

## Slide 27
[18] Metin Ersoy, AUSGANGSELEMENTE ZUM ERMITTELN DER GESTALT BEIM RECHNERGESTUTZTEN KONSTRUIEREN, Dissertation Braunschweig, 1975