## Slide 1: Unstructured Finite-Volume Arbitrary Lagrangian / Eulerian Interface Tracking computational framework for incompressible two-phase flows with surfactants
Moritz Schwarzmeier1, Suraj Raju1, Zeljko Tukovic²,
Mathis Fricke1, Dieter Bothe1, Tomislav Maric1
1 Mathematical Modeling and Analysis, TU Darmstadt ² Faculty of Mechanical Engineering and Naval Architecture, FSB Zagreb
This presentation

## Slide 2: Interface-Tracking divides the domain with a sharp interface
Finite volume
Sharp interface
Moving mesh
Arbitrary cells
[Tuković and Jasak, 2012, p. 74]
Bulk equations
Interfacial jump conditions

## Slide 3: We verify surfactant capabilities
Transport with the interface
Changing interface
Surfactant induced Marangoni effect

## Slide 4: What is the SGS and why do we need it?
with
Reactive Oxygen Taylor Bubble - Solution of Cu(btmgp)I (20 mM) in Acetonitrile at ambient pressure and temperature. Source: Project Group Prof. Dr.-Ing. Michael Schlüter, TU Hamburg: Experimental Investigation of Reactive Bubbly Flows - Influence of Boundary Layer Dynamics on Mass Transfer and Chemical Reactions
Adaption of fluxes at both sides of the first boundary cell layer

## Slide 5: For development we have simple test cases
Flat plate
Axisymmetric bubble
Position on interface
Sherwood number

## Slide 6: We added extensive evaluation possibilities, e.g.
Boundary layer thickness
The boundary layer thickness grows slowly, where the flow is adjacent. It is big, where the flow is separated.
Concentration
The concentration boundary layer is embedded into the first layer of cells adjacent to the interface over a large portion of the bubble.
Diffusivity coefficient (from inside out: at the interface, the 2nd layer, original)
In the impingement area, the flow at the interface is increased, but decreased at the cell faces between first and second cell layer. Not much correction is needed where the boundary layer thickness is big.

## Slide 7: Wrap-up
We provide an Arbitrary Lagrangian/Eulerian Interface Tracking (ALE-IT) framework for OpenFOAM
We implemented our Subgrid-scale model library
  Calculate very thin passive scalar boundary layers
  Correct diffusive and convective fluxes at the boundary and the faces next to the interface
    The fluxes at the interface are increased
    The fluxes at the faces next to the interface are decreased
  Visualisation of Subgrid-scale model internal parameters enables understanding and further developments
Publicly available soon

## Slide 8: Further reading
This presentation DOI: 10.48328/tudatalib-1266
Preprint (currently in preparation)
Code repository (currently private, going public soon) https://gitlab.com/interface-tracking/
Papers
  Interface Tracking: Zeljko
    Tuković, Ž. & Jasak, H. A moving mesh finite volume interface tracking method for surface tension dominated interfacial fluid flow. Computers & Fluids 55, 70–84 (2012).
  Subgrid-scale model
    Pesci, C., Weiner, A., Marschall, H. & Bothe, D. Computational analysis of single rising bubbles influenced by soluble surfactant. J. Fluid Mech. 856, 709–763 (2018).
    Weiner, A. & Bothe, D. Advanced subgrid-scale modeling for convection-dominated species transport at fluid interfaces with application to mass transfer from rising bubbles. Journal of Computational Physics 347, 261–289 (2017).
  Surfactant verification cases
    Antritter, T. Numerical Simulation of Coupled Wetting and Transport Phenomena in Inkjet Printing. (Technische Universität Darmstadt, 2022). doi:10.26083/tuprints-00021326.
This presentation
Code repository is coming for Christmas

## Slide 9: Appendix

## Slide 10: Flat plate
Prescribed velocity = 0.1 m/s
No velocity boundary layer
Peclet number 105
  Tested with 104 – 107

## Slide 11: Flat plate
Diffusivity [m²/s] | Peclet number [ ]
5e-08 | 1e4
5e-09 | 1e5
5e-10 | 1e6
5e-11 | 1e7

## Slide 12: Axisymmetric bubble
Prescribed velocity based on solution by Satapathy & Smith
Spherical bubble (Ø 2mm) with rigid interface
Axisymmetric setup
Schmidt-numbers of real-world problems
Diffusivity [m²/s] | Schmidt number [ ]
5e-08 | 1e4
5e-09 | 1e5
5e-10 | 1e6
5e-11 | 1e7

## Slide 13: Axisymmetric bubble
Concentration
Surface normal gradient at the surface
Surface normal gradient at outward-faces of the 1st cell layer
Accumulates pronounced in the wake of the bubble.
Decreases over the run length to almost zero in the wake.
Is highest where the flow is still adjacent. Is almost zero in the impingement area and in the center of the wake.

## Slide 14: Rotating contaminated droplet
Prescribed rotation
No mesh motion
With/without diffusivity
cf. [Antritter, 2022]

## Slide 15: Rotating contaminated droplet
Prescribed rotation
No mesh motion
With/without diffusivity
cf. [Antritter, 2022]

## Slide 16: Expanding contaminated droplet
Prescribed velocity
Prescribed mesh motion
No diffusion
cf. [Antritter, 2022]

## Slide 17: Expanding contaminated droplet
Prescribed velocity
Prescribed mesh motion
No diffusion
cf. [Antritter, 2022]

## Slide 18: Surfactant induced Marangoni effect driven bubble
No (mesh) motion, rigid bubble
Fixed surfactant concentration leads to pressure gradient